## Slide 1
Blink the LED
(Hit the Space key to input space)
Light off the LED
Order your computer to wait for a while
Light up the LED
IchigoJam first step
“WAIT120” means “wait 2sec” Q:”WAIT60” means?
Light up the LED 1sec ( to connect commands)
Hit the UP key twice.
Hit the RIGHT key 12 times.
Hit the Backspace key to delete “6”.
Type “12”. Hit the Enter to modify your order.
You can save up to four programs (0 to 3)
After reboot your computer,
you can load that program.
“RUN” is a command to start your program.
Hit the ESC key to stop the program.
Also the F5 key is same as “RUN”.
Type “LED1” and hit the Enter.
Every line needs to hit the Enter.
The F3 key types “SAVE”.
The F2 key types “LOAD”.
Type “NEW” to clear your program.
SAVE0
LOAD0
NEW
LED1
LED0
WAIT120
WAIT60
:
LED1:WAIT60:LED0
LED1:WAIT120:LED0
10 LED1:WAIT30
20 LED0:WAIT30
30 GOTO10
RUN
“LIST” is a command to display the program.
The F4 key works same way.
LIST
Can you blink the LED more fast?
The Enter to tell computer your modification.
http://ichigojam.net/

## Slide 2
http://ichigojam.net/
Baseball! (Hit any key to hit the ball)
Rafting! (The RIGHT and the LEFT key to avoid)
Screen jack! (Hit any key)
IchigoJam mini games
shift
+
(
9
Hit the Shift key to type ‘(‘, ‘)’ or ‘”’
10 CLS:X=15
20 LC X,5:?”O”
30 LC RND(32),23:?”*”
35 WAIT 3
36 X=X-BTN(28)+BTN(29)
37 IF SCR(X,5) END
40 GOTO 20
10 LET C,1:CLS
20 LC RND(32),RND(22)
30 ?CHR$(C)
40 LET K,INKEY():IF K C=K
50 GOTO 20
10 LET Y,0
20 CLS
30 LC 4,15:?”%”
40 LC 5,Y:?”O”
50 IF INKEY() GOTO 90
60 LET Y,Y+1
70 WAIT 6
80 GOTO 20
90 IF Y=15 ?”HIT!”
Type! (Type in A to Z)
Calc! (Calculate the sum quickly)
How fast? (Hit the Space key after lighting up LED)
10 LED 0
20 WAIT RND(180)+60
30 LED 1:CLT
40 IF BTN(32)=0 GOTO 40
50 ?TICK()
10 LET N,65:CLT
20 ?CHR$(N);
30 IF INKEY()!=N GOTO 30
40 LET N,N+1:IF N<91 GOTO 20
50 ?:?TICK()/60
10 LET N,0:CLT
20 LET A,RND(10)
30 LET B,RND(10)
40 ?A;”+”;B;”=“;:INPUT C
50 IF C!=A+B ?”NG!”:END
60 LET N,N+1:IF N<10 GOTO 20
70 ?TICK()/60